## Slide 1
Heather Meiring, Abhishek Pillai, Mark Rowland, Raja Vellanki
Special Thanks to Sebastian Coddington for his “cool convertible wheels”
Troop 605, home of the Fischbot Robots
Troop 605 Robotics Merit Badge

## Slide 2: Session 1
Safety and Pillia Brain

## Slide 3
This session will cover:

## Slide 5: Occupational Safety and Health Administration (OSHA)
Robotics
Studies indicate that many robot accidents occur during non-routine operating conditions, such as programming, maintenance, testing, setup, or adjustment. During many of these operations the worker may temporarily be within the robot's working envelope where unintended operations could result in injuries.

## Slide 6: Robotic Safety
SOLDERING
Soldering can be dangerous because of the heat from the iron and the chemical fumes and vapors released from the solder and flux, respectively. When soldering, observe the following points:
Wear eye and face protection.
Solder in well-ventilated areas.
Never touch the iron/gun. It heats to extreme temperatures that will cause severe burns. Wear cotton clothing that covers your arms and legs. Keep your soldering iron in its protective holder when not actually being used.
Always wash your hands with soap and water after handling solder.
Do not leave any hot tools, where someone can accidentally contact the hot element. ALWAYS ASSUME IT’S HOT!!!!

## Slide 7: Robotic Safety
STORED ENERGY
Plan out the required activities when servicing or making repairs to the robot. Make sure all teammates are aware that work is being done on the robot. Address the following:
Ensure no one is working on the robot when it will be energized during repairs.
Electrical Energy: Disconnect the electric power source
Always de-energize the robot before working on it by unplugging batteries. Open the main circuit breaker (“re-set” lever is released).
Pneumatic Energy: Always vent any compressed air to the atmosphere.
Relieve any compressed or stretched springs or tubing and lower all raised components.

## Slide 8: Robotic Safety
BATTERY SAFETY
CAUTION: Batteries contain acid. This substance, H2SO4, is a corrosive, colorless liquid that will burn your eyes, skin, and clothing.
Any battery that is visibly damaged in any way is dangerous and unusable, and should be set aside and handled accordingly.
Care must be taken when recharging batteries. Hydrogen can build up and explode.
First Aid: Neutralize it by pouring the sodium bicarbonate (baking soda) on all wetted surfaces.

## Slide 9: Robotic Safety – First Aid
Injury | First Aid
Cuts - small | Wear gloves Wash – Neosporin - Bandage
Cuts - large | Clean, bandage, apply pressure
Eye Injury - Foreign object or Chemical | Flush with water
Burn - Heat | Wash in cold water – Apply Ice – Apply Aloe
Burn - Chemical | Wash site thoroughly with soap and water
Robot becomes self aware | Have "Fail Safe" shut down switch
You become enslaved by robot | "Obey" then Plan rebellion
*** Call 911 or seek medical attention if injury is serious ***

## Slide 10: Engineering Notebook
An Engineering Notebook is a place to document your ideas and work.
It is a legal document
It can be used for Patents and Legal
Each entry should be dated
It should have references, contacts, drawings, formulas, empirical results, etc.

## Slide 11: Your Engineering Notebook Should Contain:
A description of the problem you are solving
Design ideas
List of components
Circuit Diagram
Drawings of your robot
Code listings
Experiments (challenges) and their results
Your observations
Short Summary of the project

## Slide 12
Let’s build it!
Scooter
Scout
Fischbot
605

## Slide 13: Start with the Pillia Brain 100 Computational Power to solve all our problems
What is it:
An Arduino Nano
AtMega328
  The high-performance Microchip picoPower 8-bit AVR RISC-based microcontroller combines 32KB ISP flash memory, 2KB SRAM, 23 general purpose I/O lines, 32 general purpose working registers, serial programmable USART, a 6-channel 10-bit A/D converter, The device operates at 5.5 volts @ 16MHz.
What we’ll learn:
Setup our software for programming
Basic Arduino programming
How to write a function
Controlling LEDs

## Slide 14: Software Installation
Install the Arduino IDE
https://www.arduino.cc/en/main/software
Scroll down and select the older Legacy IDE (1.8.X)
Install it
Install the CH340 Serial Drivers
Windows CH340 Driver
Macintosh Drivers for CH340 Driver
Install NewPing Library
In the Arduino Editor Sketch-> include Library ->Manage Libraries
In the search bar enter “NewPing”
Press the install button
Install VarSpeedServo Library
https://github.com/netlabtoolkit/VarSpeedServo
Press the green code button
Download ZIP
In Arduino Sketch->include Library->Add .ZIP Library
Select the downloaded ZIP file

## Slide 15: Arduino IDE
Test your connection with Blink
Look under File->Examples->Basic->Blink
Using the Interactive Arduino Development Environment

## Slide 16: Blink Program
void setup() {
// initialize digital pin LED_BUILTIN as an output.
pinMode(LED_BUILTIN, OUTPUT);
}
void loop() {
digitalWrite(LED_BUILTIN, HIGH);) delay(1000);
digitalWrite(LED_BUILTIN, LOW); delay(1000);
}
Setup
Main Loop

## Slide 17
The PilliaBot 100:
Specializes in computational abilities
And will provide the brains of our project
Blinking
Light
What we’ll learn:
Setup our software for programming
Basic Arduino programming
Controlling LEDs
Can you make the PilliaBot signal SOS?
Challenge:
Can you make a function that turns on the LED for a given number of ms?
Challenge:

## Slide 18: Now Add These Libraries
In the menu select “sketch” -> “include libraries” -> “manage libraries …” or press “CTRL + SHIFT + I
Then search for “NewPing” and install the library
Then close the window

## Slide 19: Session 2
The Robotics Industry and the Meiring Control System

## Slide 20
Our progress

## Slide 22: Fields of Robotics
Human-Robot Interface
Mobility – Movement
Manipulation – interacting with the environment
Programming – robotic control and functionality
Sensors – real world feedback

## Slide 23: Home Work
Pick a field of robotics to discuss with your counselor.
  Find an image that aids in your discussion
Update your engineering notebook

## Slide 24: MCS: The Meiring Control System 200 Using Sonic and Servo Technology
What is it:
HC-SR04 Sonic Depth Sensor
Uses sound to measure distance to objects
It uses two types of servos for locomotion
What we’ll learn:
How a sonic sensor works
How to add library’s for Arduino
How to use a serial monitor
How to use if statements
How to read a schematic
How to build a circuit

## Slide 25: The HC SR04 Sonic Sensor

## Slide 26: Using the Sonic Sensor

## Slide 27: Document in your Engineering Journal
Circuit diagrams
Code
Tests
What is this?
The original 605 Fischbot from 2020
It’s not cute but it gave us something to build over Zoom during Covid and we earned a merit badge

## Slide 28: Scooter Schematic
FS90R Servos (360)
SG90 Servos (180)
Left Wheel 360 (Servo 2)
Right Wheel 360
(Servo 3)
Left Leg 180
(Servo 4)
Right Leg 180
(Servo 5)
Make sure both jacks are oriented this way
HC SR04
Sonic Sensor
Servo Board
Arduino Nano
Processor
Yellow wire must be next to the processor (incorrect will cause damage)
Link to Scooter Repository
https://github.com/martintrowland/Scooter

## Slide 29: Programming Arduino for the HC SR04
#include <NewPing.h>
const int LEFT_SENSOR_TRIG_PIN=8;
const int LEFT_SENSOR_ECHO_PIN=9;
const int MAX_DISTANCE=200; // max distance in cm
NewPing Sonar(LEFT_SENSOR_TRIG_PIN,LEFT_SENSOR_ECHO_PIN,MAX_DISTANCE);
int sonar(const char *label) {
int Distance = Sonar.ping_cm();
if (Distance == 0) {
Distance = MAX_DISTANCE;
}
return Distance;
}
void setup() {
// put your setup code here, to run once:
Serial.begin(115200);
delay(5000);
}
void loop() {
// put your main code here, to run repeatedly:
int Distance=sonar(“main”);
Serial.print("Ping: ");
Serial.print(Distance);
Serial.println("cm");
delay(1000);
}
Definitions
Setup
Main Loop
Functions

## Slide 30: Testing the HC SR04
HC SR04 wired to the Nano and Servo Controller board
Use Servo Controller pins 8 -> SR04 Trigger and 9-> SR04 Echo
Then test it out with the following code

## Slide 31: Controlling a FS90R Servo (360 degrees)
An electrical motor that does 360 degree rotation
Use the write command to control the motor
  write(speed, NA, false);
  The speed variable is a value 0 to 179
  0-89 causes a clockwise rotation: 0 fastest and 89 slowest
  90 stops the motor
  91-180 causes a counter clockwise rotation: 91 slowest and 179 is the fastest
Programming
  const int LEFT_WHEEL_PIN = 2
  const int LEFT_WHEEL_FORWARD = 100;
  const int LEFT_WHEEL_STOP = 90;
  const int LEFT_WHEEL_BACKWARD = 80;
  const int NA = 50; //Not Applicable
  VarSpeedServo leftWheel; //definition
  .
  leftWheel.attach(LEFT_WHEEL_PIN);
  leftWheel.write(LEFT_WHEEL_FORWARD, NA, false);
  Delay(2000);
  leftWheel.write(LEFT_WHEEL_STOP, NA, false);
  leftWheel.detach();
FS90R Speed Parameter
90
Stop
0 - 89
Fast Slow
Clockwise
91 - 179
Slow Fast
Counter
Clockwise

## Slide 32: Controlling an SG90 Servo (180 degrees)
An electrical motor that can move to an angle from 0-180 degrees
Use the write command to control the motor
  write(angle, speed, wait);
  Angle is a value 0 to 179
  Speed to move to the specified angle is 0 slowest to 255 fastest
  Wait: true causes the computer to wait until the angle of the servo reaches angle false allows the program to continue while the servo rotates to angle
Programming
  const int LEFT_LEG_PIN = 4;
  const int SLOW_SPEED = 20;
  const int LEFT_LEG_UP = 160;
  const int LEFT_LEG_DOWN = 75;
  VarSpeedServo leftLeg; //definition
  .
  leftLeg.attach(LEFT_LEG_PIN);
  leftLeg.write(LEFT_LEG_DOWN, SLOW_SPEED, true);
  Delay(2000);
  leftLeg.write(LEFT_LEG_UP, SLOW_SPEED, true);
  leftLeg.detach();
SG90 Left Leg Angle Parameter
160
Up
75
Down

## Slide 33: Add the Servos
Add the Servo motors
FS90R Servos (360)
  Servo Pin 2
  Servo Pin 3
SG90 Servos (180)
  Servo Pin 4
  Servo Pin 5
Be careful to have the
Yellow wire placed on the blue pins of the servo board. Don’t connect them to the blue pins!!! Bad things could happen!

## Slide 34: Definition Code for Servos
#include <NewPing.h>
#include <VarSpeedServo.h>
const int SONIC_TRIGGER_PIN = 8; // Arduino pin tied to trigger pin on the ultrasonic sensor.
const int SONIC_ECHO_PIN = 9; // Arduino pin tied to echo pin on the ultrasonic sensor.
const int LEFT_FOOT_PIN = 2; //Arduino PIN connection
const int RIGHT_FOOT_PIN = 3;
const int LEFT_LEG_PIN = 4;
const int RIGHT_LEG_PIN = 5;
const int MAX_DISTANCE = 200; // Maximum distance we want to ping for (in centimeters). Maximum sensor distance is rated at 400-500cm.
const int COLLISION_DISTANCE = 40; // in centimeters
const int SHUTDOWN_TIMER = 10000;
const int NA = 50; //Not Apllicable
const int SLOW_SPEED = 20;
const int MED_SPEED = 40;
const int FAST_SPEED = 200;
//defined for FS90R Servos
const int LEFT_WHEEL_FORWARD = 100;
const int LEFT_WHEEL_STOP = 89;
const int LEFT_WHEEL_BACKWARD = 80;
const int RIGHT_WHEEL_FORWARD = 80;
const int RIGHT_WHEEL_STOP = 90;
const int RIGHT_WHEEL_BACKWARD = 100;
// angle for SG90 Servos
const int RIGHT_LEG_UP = 10;
const int RIGHT_LEG_DOWN = 90;
const int LEFT_LEG_UP = 160;
const int LEFT_LEG_DOWN = 75;
//Create objects for the sonar and servos
NewPing Sonar(SONIC_TRIGGER_PIN, SONIC_ECHO_PIN, MAX_DISTANCE); // NewPing setup of pins and maximum distance.
VarSpeedServo leftWheel, rightWheel, leftLeg, rightLeg; //define Servo Variables
Definitions

## Slide 35: Add testLegs() Routine
/////////////////////////////////////////////////////////////
//-- DIAGNOSTICS ----------------------------------------------//
/////////////////////////////////////////////////////////////
void testLegs() {
Serial.println("Right Leg down");
rightLeg.write(RIGHT_LEG_DOWN, SLOW_SPEED, true);
delay(2000);
Serial.println("Right Leg up");
rightLeg.write(RIGHT_LEG_UP, SLOW_SPEED, true);
delay(2000);
Serial.println("Left Leg Down");
leftLeg.write(LEFT_LEG_DOWN, SLOW_SPEED, true);
delay(2000);
Serial.println("Right Wheel Forward");
rightWheel.write(RIGHT_WHEEL_FORWARD, NA, true);
delay(5000);
rightWheel.write(RIGHT_WHEEL_STOP, NA, true);
Serial.println("Left Wheel Forward");
leftLeg.write(LEFT_WHEEL_FORWARD, NA, true);
delay(5000);
leftLeg.write(LEFT_WHEEL_STOP, NA, true);
}
/////////////////////////////////////////////////////////////
//-- Attach/Detach Servos ----------------------------------------//
/////////////////////////////////////////////////////////////
void attachServos() {
leftWheel.attach(LEFT_WHEEL_PIN);
rightWheel.attach(RIGHT_WHEEL_PIN);
leftLeg.attach(LEFT_LEG_PIN);
rightLeg.attach(RIGHT_LEG_PIN);
}
void detachServos() {
leftWheel.detach();
rightWheel.detach();
leftLeg.detach();
rightLeg.detach();
}
Functions

## Slide 36: Session 3
Robot Design and the Coddington Chassis

## Slide 37
Our progress

## Slide 39: Robotic Competitions
B.E.S.T Robotics Design Contest
Botball Educational Robotics Program
FIRST: Robotics Competition
FIRST: Tech Challenge
National Robotics Challenge
Descriptions of these competitions:
https://blog.collegevine.com/5-robotics-competitions-for-high-schoolers/

## Slide 40: The Coddington Chassis 300 Walk and Roll with this Super Cool Chassis
What is it:
A super cool mechanic that enables both walking and wheeled locomotion.
Developed by Sebastian Coddington (my favorite robotics hobbyist)
Check out his many robotic designs on the internet.
What we’ll learn:
How to assemble the leg and wheels chassis
How to set up the correct orientation of the legs with the SG90 servos
How to integrate the electronics into the robot chasis

## Slide 41: Left Foot SG90
Add Left SG90 Servo to the left Leg
Thread cord through slot
Screw servo into left leg bracket.

## Slide 42: Left Foot FS90R
Add Left FS90R (360) servo to left bracket
Thread the wire through the channel and out the top
FS90R

## Slide 43: Assemble the Right Leg and Chassis
Repeat the same assembly for the right leg
Insert the legs into the leg chassis
Thread the wires through the slots
The picture shows the back of the chassis
The FS90R wires should thread the front of the chassis
The SG90 wires should be towards the back
Screw the wheels using the 180 degree bracket to the FS90R servos
Do both sides (Left/Right)

## Slide 44: Calibrating the SG90 Servors
We need to set the SG90 Servo Orientation
  Set the right leg SG90 servo to 10 (degrees)
  Set the left leg SG90 servo to 160 (degrees)
  Load and Run the script to set the orientation
    GitHubhttps://github.com/martintrowland/Scooter/blob/main/Scooter_2_servos.ino
  Lock the leg into this position by screwing the bracket into the servo with the legs in the up position.

## Slide 45: Session 4
Robot Design and the Vellanki Cap

## Slide 47: Robotics Careers
The career choices for robotics are almost endless but here are a few examples
  - Automotive Industry
  - NASA
  - Boston Dynamics
  - Software Engineering
  - Consumer Markets
  - Household robots
  - Prosthetics
  - Military

## Slide 48: Education for a Robotics Career
Electrical Engineering (Sensors, computation)
  Control Systems (Mobility)
Computer Engineering (Programming, computation, human-robot interface)
Robotic Engineering (human-robot interface, system integration)
Computer Science (Programming, AI, ML)
Mechanical Engineering (manipulators, mobility)
Bio-Medical Engineering (medical robots)
https://www.youtube.com/watch?v=zauYACP2lOc
OSU Collaborative Robotics Institute

## Slide 49: The Vellanki Cap 400 Scooter’s Styling Top
What is it:
Scooter’s head and brain
What we’ll learn:
Soldering and burning
How to fit a lot of wiring and compute in a small space
How cool he looks in a cap!

## Slide 50: Scooter Schematic
FS90R Servos (360)
SG90 Servos (180)
Left Wheel 360 (Servo 2)
Right Wheel 360
(Servo 3)
Left Leg 180
(Servo 4)
Right Leg 180
(Servo 5)
Make sure both jacks are oriented this way
HC SR04
Sonic Sensor
Servo Board
Arduino Nano
Processor
Yellow wire must be next to the processor (incorrect will cause damage)
Link to Scooter Repository
https://github.com/martintrowland/Scooter

## Slide 51: The Vellanki Cap 400 Scooter’s Styling Top
Add the Servo Connections to the Servo Control Board (Orange wire to Blue pin)
  Pin 2: FS90 360 Servo Left Wheel
  Pin 3: FS90 360 Servo Right Wheel
  Pin 4: SG90 Servo Left Leg
  Pin 5: SG90 Servo Right Leg
Add the Sonar
  Pin 8: Trigger (Blue pin)
  Pin 9: Echo (Blue pin), VCC (Red), GND (Black)
Connect the 9 Volt Battery

## Slide 52: The Vellanki Cap 400 Scooter’s Styling Top
If only he had a brain…

## Slide 53
Plug the USB cable to Scooter
Time to run diagnostics:
Scooter_1_sonar.ino
Scooter_2_servos.ino
Check the Sonar readings using the Arduino watch window
Check that the Servos are activating

## Slide 54: Session 5
Robot Design and the Coddington Chassis

## Slide 55
Our progress

## Slide 57: Let’s put all the tech of the Pillia Brain, the Meiring Control System, and into one and what do you get? A FischBot 605 Robot named Scooter
What is it:
An autonomous robot
Utilizes depth sensors and locomotion to avoid obstacles
What we’ll learn:
Algorithms for Obstacle avoidance
How to debug
Challenges in navigation

## Slide 58: Scooter Navigation
if no object is in front, go forward
if an obstacle is in front, stop
Sonar
Sensor
Scooter
Forward
Sonar
Sensor
Stop
WALL
Scooter

## Slide 59: Scooter Navigation
Look left, is there an obstacle?
Avoid Obstacle
Sonar
Sensor
Scooter
WALL
Sonar
Sensor
Scooter
WALL
Avoid Obstacle
Look right, is there an obstacle?
Choose the direction that has the farthest clear path
WALL
WALL

## Slide 60: BONUS Problem: What if both directions are blocked?
Avoid Obstacle
Sonar
Sensor
WALL
Scooter
Sonar
Sensor
Scooter
Rotate until we find a clear path
WALL
WALL
Avoid Obstacle
WALL
WALL
WALL

## Slide 61: Let’s program the Navigation

## Slide 62: Initialization and Constants
Include the librarys
  NewPing for the sonar
  VarSpeedSerco for controlling the servo motors
Set the pin assignments
Define MAX_DISTANCE for farthest sonar reading
Define COLLISION_DISTANCE for how close to get to a wall before stopping
The Speed constants define wheel speeds
Define Left and Right Wheel movement:
  Forward
  Backward
  Stop
Define Leg Positions
  Up
  Down
//----------------------------------------------------------------
//-- Mark Rowland
//-- Troop 605 Robotics Merit Badge
#include <NewPing.h>
#include <VarSpeedServo.h>
const int DEBUG = true;
const int LEFT_WHEEL_PIN = 2; //Arduino PIN connection
const int RIGHT_WHEEL_PIN = 3;
const int LEFT_LEG_PIN = 4;
const int RIGHT_LEG_PIN = 5;
const int SONIC_TRIGGER_PIN = 8; // Arduino pin tied to trigger pin on the ultrasonic sensor.
const int SONIC_ECHO_PIN = 9; // Arduino pin tied to echo pin on the ultrasonic sensor.
const int MAX_DISTANCE = 200; // Maximum distance we want to ping for (in centimeters)
const int COLLISION_DISTANCE = 40; // in centimeters
const int NA = 50; //Not Applicable
const int SLOW_SPEED = 20;
const int MED_SPEED = 40;
const int FAST_SPEED = 200;
const int LEFT_WHEEL_FORWARD = 100;
const int LEFT_WHEEL_STOP = 89;
const int LEFT_WHEEL_BACKWARD = 80;
const int RIGHT_WHEEL_FORWARD = 80;
const int RIGHT_WHEEL_STOP = 90;
const int RIGHT_WHEEL_BACKWARD = 100;
const int RIGHT_LEG_UP = 10;
const int RIGHT_LEG_DOWN = 90;
const int LEFT_LEG_UP = 160;
const int LEFT_LEG_DOWN = 75;
NewPing Sonar(SONIC_TRIGGER_PIN, SONIC_ECHO_PIN, MAX_DISTANCE); //setup Sonar
VarSpeedServo leftWheel, rightWheel, leftLeg, rightLeg;
https://github.com/martintrowland/Scooter/blob/main/Scooter_3_movement.ino

## Slide 63: Setup Subroutines
Setup is the first routine
https://github.com/martintrowland/Scooter/blob/main/Scooter_3_movement.ino
///////////////////////////////////////////////////////////////////
//-- Setup ------------------------------------------------------//
///////////////////////////////////////////////////////////////////
void attachServos() {
leftWheel.attach(LEFT_WHEEL_PIN);
rightWheel.attach(RIGHT_WHEEL_PIN);
leftLeg.attach(LEFT_LEG_PIN);
rightLeg.attach(RIGHT_LEG_PIN);
}
void detachServos() {
leftWheel.detach();
rightWheel.detach();
leftLeg.detach();
rightLeg.detach();
}
void setup() {
Serial.begin(115200); // Open serial monitor at 115200 baud to see ping results.
attachServos();
leftLeg.write(LEFT_LEG_UP, FAST_SPEED, true);
rightLeg.write(RIGHT_LEG_UP, FAST_SPEED, true);
leftWheel.write(LEFT_WHEEL_STOP, NA, true);
rightWheel.write(RIGHT_WHEEL_STOP, NA, true);
delay(3000);
}

## Slide 64: Basic Robot Movement
Let’s create a subroutine to stop the wheels
  Name it wheelsStop(int duration)
  Use commands like:
    rightWheel.write(RIGHT_WHEEL_STOP, NA, false);
    leftWheel.write(LEFT_WHEEL_STOP, NA, false);
    leftWheel.wait();
    rightWheel.wait();
Create wheelsForward(int duration) routine
  Use commands like
    leftWheel.write(LEFT_WHEEL_FORWARD, NA, false);

## Slide 65: Autonomous Forward
Sonar
Sensor
Forward
const int COLLISION_DISTANCE=40;
distance=sonar();
if (distance>COLLISION_DISTANCE){
wheelsForward(400);
}
If no object is closer than COLLISION_DISTANCE then go Forward
Code
Robot
COLLISION_DISTANCE is the distance in which the object is too close to steer around to avoid.
By experiment this is about 40cm

## Slide 66: STOP
COLLISION_DISTANCE
COLLISION_DISTANCE is the distance in which the object is too close to steer around to avoid.
By experiment this is about 40cm
If an object is closer than the COLLISION_DISTANCE in either the right or left side, then stop
Code
Sonar
Sensor
Stop
WALL
40 cm
const in COLLISION_DISTANCE=40;
distance=sonar();
if (distance>COLLISION_DISTANCE){
wheelsForward(400);
}else{
lookLeft();
}
Look left, is there an obstacle?
Avoid Obstacle
Sonar
Sensor
Scooter
WALL
WALL

## Slide 67: Look Left
Look left, is there an obstacle?
Avoid Obstacle
Sonar
Sensor
Scooter
WALL
WALL

## Slide 68: Scooter Navigation
Right
Sensor
Left
Sensor
Forward
Right
Sensor
Left
Sensor
WALL
Stop
if an object isn’t close go forward
if an obstacle is really close to both the right and left sensor stop

## Slide 69: FischBot Navigation
Right
Sensor
Left
Sensor
Right
Sensor
Left
Sensor
WALL
Turn Right
Turn Left
WALL
if an object is close to the right sensor turn left
if an object is close to the left sensor turn right

## Slide 70: What’s a Conditional Statement
In English
IF the distance is less than a mile then I’ll walk
ELSE if the distance is less than five miles then I’ll take a bus
ELSE if the distance is less than 100 miles then I’ll drive a car
ELSE take a plane
Examples in Arduino (C Language):
if (condition) {
Action;
}else if (condition) {
Action;
}else {
Action;
}
Condition
Action
If(distance<1){
Serial.println(“let’s walk”);
}else if (distance<5){
Serial.println(“let’s take a bus”);
}else if (distance<100){
Serial.println(“let’s drive”);
else{
Serial.println(“Let’s fly!!”);
}

## Slide 71: Tune and Demonstrate your Robot
Can you get your FischBot to navigate through a series of obstacles?
Challenge:
Can you tune your robot to go straight?
Left?
Right?
Challenge:
Can you write code such that your FischBot tries to travel in the same direction while avoiding obstacles?
How would you do it?
Super Challenge:

## Slide 72: BACKUP

## Slide 73: Uninstalling From Macinstosh
A couple of Mac users have said “the driver crashes my mac Sierra how do I uninstall”.
Firstly regards the crash make sure you installed the 1.3 version of the driver, not the old one. You could download it directly from the Manufacturers Website in case they have issued an update since I wrote this page.
Secondly a quick google search reveals that this is how you uninstall:
Open a terminal and type: cd /Library/Extensions/
Verify that the .kext file is present: ls | grep usbserial.kext
Output should be: usbserial.kext
Then type: sudo rm -R usbserial.kext
Verify that the .kext file has been removed: ls | grep usbserial.kext
Output should be empty.
After you should remove the files stored in receipts folder: cd /private/var/db/receipts/
Find the enties: ls | grep usbserial*
Output should be: codebender.cc.ch34xinstaller.usbserial.pkg.bom codebender.cc.ch34xinstaller.usbserial.pkg.plist
Remove each one of the files of the above list: sudo rm -r filename`

## Slide 74: Locomotion Code
#define RIGHT_MOTOR_PIN 5
#define LEFT_MOTOR_PIN 6
#define LEFT_VIBRATE 150
#define RIGHT_VIBRATE 150
#define VIBRATE 150
#define NO_VIBRATE 0
void setup() {
Serial.begin(115200); // Open serial monitor at 115200 baud to see ping results.
pinMode(RIGHT_MOTOR_PIN, OUTPUT);
pinMode(LEFT_MOTOR_PIN, OUTPUT);
delay(5000);
}
void standStill(int seconds) {
analogWrite(RIGHT_MOTOR_PIN, NO_VIBRATE);
analogWrite(LEFT_MOTOR_PIN, NO_VIBRATE);
Serial.println("stop");
delay(seconds * 1000);
}
void turnLeft(int seconds) {
analogWrite(RIGHT_MOTOR_PIN, VIBRATE);
analogWrite(LEFT_MOTOR_PIN, NO_VIBRATE);
Serial.println("turn left");
delay(seconds * 1000);
standStill(0);
}
void turnRight(int seconds) {
analogWrite(RIGHT_MOTOR_PIN, NO_VIBRATE);
analogWrite(LEFT_MOTOR_PIN, VIBRATE);
Serial.println("turn right");
delay(seconds * 1000);
standStill(0);
}
void turnRight(int seconds) {
analogWrite(RIGHT_MOTOR_PIN, NO_VIBRATE);
analogWrite(LEFT_MOTOR_PIN, VIBRATE);
Serial.println("turn right");
delay(seconds * 1000);
standStill(0);
}
void goForward(int seconds) {
analogWrite(RIGHT_MOTOR_PIN, RIGHT_VIBRATE);
analogWrite(LEFT_MOTOR_PIN, LEFT_VIBRATE);
Serial.println("go forward");
delay(seconds * 1000);
standStill(0);
}
void calibrateMovement() {
goForward(5);
standStill(5);
turnLeft(5);
standStill(5);
turnRight(5);
standStill(5);
while (1) {};
}
void loop() {
calibrateMovement();
}

## Slide 75
Classification: Top Secret
Model: Fischbot 605
Name: Scooter Scout

## Slide 76
FischBot 500
Troop 605
Robotics Merit Badge
Contents:
1 x bread board
1x Arduino Nano CPU
1 x 3 pin switch
1 x 9V Battery with tape
1x 9V Battery Connector
2x HC SR04 Depth Sensors
2x Cell phone motor Vibrators
20x jumper wires
FischBot 500
Troop 605
Robotics Merit Badge
FischBot 500
Troop 605
Robotics Merit Badge
Contents:
1 x bread board
1x Arduino Nano CPU
1 x 3 pin switch
1 x 9V Battery with tape
1x 9V Battery Connector
2x HC SR04 Depth Sensors
2x Cell phone motor Vibrators
20x jumper wires
Contents:
1 x bread board
1x Arduino Nano CPU
1 x 3 pin switch
1 x 9V Battery with tape
1x 9V Battery Connector
2x HC SR04 Depth Sensors
2x Cell phone motor Vibrators
20x jumper wires