## Slide 1
Heather Meiring, Abhishek Pillai, Mark Rowland,
Special Thanks to Sebastian Coddington for his “cool convertible wheels”
Troop 605, home of the Fischbot Robots
Troop 605 Robotics Merit Badge

## Slide 2: Session 1
Safety

## Slide 3
This session will cover:

## Slide 5: Occupational Safety and Health Administration (OSHA)
Robotics
Studies indicate that many robot accidents occur during non-routine operating conditions, such as programming, maintenance, testing, setup, or adjustment. During many of these operations the worker may temporarily be within the robot's working envelope where unintended operations could result in injuries.

## Slide 6: Robotic Safety
SOLDERING
Soldering can be dangerous because of the heat from the iron and the chemical fumes and vapors released from the solder and flux, respectively. When soldering, observe the following points:
Wear eye and face protection.
Solder in well-ventilated areas.
Never touch the iron/gun. It heats to extreme temperatures that will cause severe burns. Wear cotton clothing that covers your arms and legs. Keep your soldering iron in its protective holder when not actually being used.
Always wash your hands with soap and water after handling solder.
Do not leave any hot tools, where someone can accidentally contact the hot element. ALWAYS ASSUME IT’S HOT!!!!

## Slide 7: Robotic Safety
STORED ENERGY
Plan out the required activities when servicing or making repairs to the robot. Make sure all teammates are aware that work is being done on the robot. Address the following:
Ensure no one is working on the robot when it will be energized during repairs.
Electrical Energy: Disconnect the electric power source
Always de-energize the robot before working on it by unplugging batteries. Open the main circuit breaker (“re-set” lever is released).
Pneumatic Energy: Always vent any compressed air to the atmosphere.
Relieve any compressed or stretched springs or tubing and lower all raised components.

## Slide 8: Robotic Safety
BATTERY SAFETY
CAUTION: Batteries contain acid. This substance, H2SO4, is a corrosive, colorless liquid that will burn your eyes, skin, and clothing.
Any battery that is visibly damaged in any way is dangerous and unusable, and should be set aside and handled accordingly.
Care must be taken when recharging batteries. Hydrogen can build up and explode.
First Aid: Neutralize it by pouring the sodium bicarbonate (baking soda) on all wetted surfaces.

## Slide 9: Robotic Safety – First Aid
Injury | First Aid
Cuts - small | Wear gloves Wash – Neosporin - Bandage
Cuts - large | Clean, bandage, apply pressure
Eye Injury - Foreign object or Chemical | Flush with water
Burn - Heat | Wash in cold water – Apply Ice – Apply Aloe
Burn - Chemical | Wash site thoroughly with soap and water
Robot becomes self aware | Have "Fail Safe" shut down switch
You become enslaved by robot | "Obey" then Plan rebellion
*** Call 911 or seek medical attention if injury is serious ***

## Slide 10: Engineering Notebook
An Engineering Notebook is a place to document your ideas and work.
It is a legal document
It can be used for Patents and Legal
Each entry should be dated
It should have references, contacts, drawings, formulas, empirical results, etc.

## Slide 11: Your Engineering Notebook Should Contain:
A description of the problem you are solving
Design ideas
List of components
Circuit Diagram
Drawings of your robot
Code listings
Experiments (challenges) and their results
Your observations
Short Summary of the project

## Slide 12
Let’s build it!
Scooter
Scout
Fischbot
605

## Slide 13: Start with the PilliaBot 100 Computational Power to solve all our problems
What is it:
An Arduino Nano
AtMega328
  The high-performance Microchip picoPower 8-bit AVR RISC-based microcontroller combines 32KB ISP flash memory, 2KB SRAM, 23 general purpose I/O lines, 32 general purpose working registers, serial programmable USART, a 6-channel 10-bit A/D converter, The device operates at 5.5 volts @ 16MHz.
What we’ll learn:
Setup our software for programming
Basic Arduino programming
How to write a function
Controlling LEDs

## Slide 14: Software Installation
Arduino IDE
https://www.arduino.cc/en/main/software
CH340 Serial Drivers
Windows CH340 Driver
Macintosh Drivers for CH340 Driver

## Slide 15: Arduino IDE
Test your connection with Blink
Look under File->Examples->Basic->Blink
Using the Interactive Arduino Development Environment

## Slide 16: Blink Program
void setup() {
// initialize digital pin LED_BUILTIN as an output.
pinMode(LED_BUILTIN, OUTPUT);
}
void loop() {
digitalWrite(LED_BUILTIN, HIGH);) delay(1000);
digitalWrite(LED_BUILTIN, LOW); delay(1000);
}

## Slide 17
The PilliaBot 100:
Specializes in computational abilities
And will provide the brains of our project
Blinking
Light
What we’ll learn:
Setup our software for programming
Basic Arduino programming
Controlling LEDs
Can you make the PilliaBot signal SOS?
Challenge:
Can you make a function that turns on the LED for a given number of ms?
Challenge:

## Slide 18: Now Add These Libraries
In the menu select “sketch” -> “include libraries” -> “manage libraries …” or press “CTRL + SHIFT + I
In the search type “servo” then select “install”
Then search for “NewPing” and install the library
Then close the window

## Slide 19: Session 2
The Robotics Industry

## Slide 20
Our progress

## Slide 22: Fields of Robotics
Human-Robot Interface
Mobility – Movement
Manipulation – interacting with the environment
Programming – robotic control and functionality
Sensors – real world feedback

## Slide 23: Home Work
Pick a field of robotics to discuss with your counselor.
  Find an image that aids in your discussion
Update your engineering note book

## Slide 24: MCS: The Meiring Control System 200 Using Sonic and Servo Technology
What is it:
HC-SR04 Sonic Depth Sensor
Uses sound to measure distance to objects
It uses two types of servos for locomotion
What we’ll learn:
How a sonic sensor works
How to add library’s for Arduino
How to use a serial monitor
How to use if statements
How to read a schematic
How to build a circuit

## Slide 25: The HC SR04 Sonic Sensor

## Slide 26: Using the Sonic Sensor

## Slide 27: Document in your Engineering Journal
Circuit diagrams
Code
Tests
What is this?
The original 605 Fischbot from 2020
It’s not cute but it gave us something to build over Zoom during Covid and we earned a merit badge

## Slide 28: Scooter Schematic
FS90R Servos (360)
SG90 Servos (180)
Left Wheel 360 (Servo 2)
Right Wheel 360
(Servo 3)
Left Leg 180
(Servo 4)
Right Leg 180
(Servo 5)
Make sure both jacks are oriented this way
HC SR04
Sonic Sensor
Servo Board
Arduino Nano
Processor
Yellow wire must be next to the processor (incorrect will cause damage)
Link to Scooter Code

## Slide 29: Programming Arduino for the HC SR04
#include <NewPing.h>
const int LEFT_SENSOR_TRIG_PIN=8;
const int LEFT_SENSOR_ECHO_PIN=9;
const int MAX_DISTANCE=200; // max distance in cm
NewPing sonar(LEFT_SENSOR_TRIG_PIN,LEFT_SENSOR_ECHO_PIN,MAX_DISTANCE);
int sonar(const char *label) {
int Distance = Sonar.ping_cm();
if (Distance == 0) {
Distance = MAX_DISTANCE;
}
return Distance;
}
void setup() {
// put your setup code here, to run once:
Serial.begin(115200);
delay(5000);
}
void loop() {
// put your main code here, to run repeatedly:
int Distance=sonar(“main”);
Serial.print("Ping: ");
Serial.print(Distance);
Serial.println("cm");
delay(1000);
}
Definitions
Setup
Main Loop
Functions

## Slide 30: Testing the HC SR04
HC SR04 wired to the Nano and Servo Controller board
Use Servo Controller pins 8 -> SR04 Trigger and 9-> SR04 Echo
Then test it out with the following code

## Slide 31: Controlling a FS90R Servo (360 degrees)
An electrical motor that does 360 degree rotation
Use the write command to control the motor
  write(speed, NA, false);
  The speed variable is a value 0 to 179
  0-89 causes a clockwise rotation: 0 fastest and 89 slowest
  90 stops the motor
  91-180 causes a counter clockwise rotation: 91 slowest and 179 is the fastest
Programming
  const int LEFT_WHEEL_PIN = 2
  const int LEFT_WHEEL_FORWARD = 100;
  const int LEFT_WHEEL_STOP = 90;
  const int LEFT_WHEEL_BACKWARD = 80;
  const int NA = 50; //Not Applicable
  VarSpeedServo leftWheel; //definition
  .
  leftWheel.attach(LEFT_WHEEL_PIN);
  leftWheel.write(LEFT_WHEEL_FORWARD, NA, false);
  Delay(2000);
  leftWheel.write(LEFT_WHEEL_STOP, NA, false);
  leftWheel.detach();
FS90R Speed Parameter
90
Stop
0 - 89
Fast Slow
Clockwise
91 - 179
Slow Fast
Counter
Clockwise

## Slide 32: Controlling an SG90 Servo (180 degrees)
An electrical motor that can move to an angle from 0-180 degrees
Use the write command to control the motor
  write(angle, speed, wait);
  Angle is a value 0 to 179
  Speed to move to the specified angle is 0 slowest to 255 fastest
  Wait: true causes the computer to wait until the angle of the servo reaches angle false allows the program to continue while the servo rotates to angle
Programming
  const int LEFT_LEG_PIN = 4;
  const int SLOW_SPEED = 20;
  const int LEFT_LEG_UP = 160;
  const int LEFT_LEG_TILT = 100;
  const int LEFT_LEG_DOWN = 75;
  const int LEFT_LEG_EXTEND = 40;
  VarSpeedServo leftLeg; //definition
  .
  leftLeg.attach(LEFT_LEG_PIN);
  leftWheel.write(LEFT_LEG_DOWN, SLOW_SPEED, true);
  Delay(2000);
  leftWheel.write(LEFT_LEG_UP, SLOW_SPEED, true);
  leftWheel.detach();
SG90 angle Parameter
180
Right
0
Left
90
Middle

## Slide 33: Add the Motors
Add the Servo motors
FS90R Servos (360)
  Servo Pin 2
  Servo Pin 3
SG90 Servos (180)
  Servo Pin 4
  Servo Pin 5
Be careful to have the
Yellow wire placed on the blue pins of the servo board. Don’t connect them to the blue pins!!! Bad things could happen!

## Slide 34: Definition Code for Servos
#include <NewPing.h>
#include <VarSpeedServo.h>
const int SONIC_TRIGGER_PIN = 8; // Arduino pin tied to trigger pin on the ultrasonic sensor.
const int SONIC_ECHO_PIN = 9; // Arduino pin tied to echo pin on the ultrasonic sensor.
const int LEFT_FOOT_PIN = 2; //Arduino PIN connection
const int RIGHT_FOOT_PIN = 3;
const int LEFT_LEG_PIN = 4;
const int RIGHT_LEG_PIN = 5;
const int MAX_DISTANCE = 200; // Maximum distance we want to ping for (in centimeters). Maximum sensor distance is rated at 400-500cm.
const int COLLISION_DISTANCE = 40; // in centimeters
const int SHUTDOWN_TIMER = 10000;
const int NA = 50; //Not Apllicable
const int SLOW_SPEED = 20;
const int MED_SPEED = 40;
const int FAST_SPEED = 200;
//defined for FS90R Servos
const int LEFT_WHEEL_FORWARD = 100;
const int LEFT_WHEEL_STOP = 89;
const int LEFT_WHEEL_BACKWARD = 80;
const int RIGHT_WHEEL_FORWARD = 80;
const int RIGHT_WHEEL_STOP = 90;
const int RIGHT_WHEEL_BACKWARD = 100;
// angle for SG90 Servos
const int RIGHT_LEG_UP = 10;
const int RIGHT_LEG_DOWN = 90;
const int LEFT_LEG_UP = 160;
const int LEFT_LEG_DOWN = 75;
//Create objects for the sonar and servos
NewPing Sonar(SONIC_TRIGGER_PIN, SONIC_ECHO_PIN, MAX_DISTANCE); // NewPing setup of pins and maximum distance.
VarSpeedServo leftWheel, rightWheel, leftLeg, rightLeg; //define Servo Variables
Definitions

## Slide 35: Calibrating the SG90 Servors
We need to set the SG90 Servo Orientation
  Set the right leg SG90 servo to 10 (degrees)
  Set the left leg SG90 servo to 160 (degrees)
  Load and Run the script to set the orientation
    GitHubhttps://github.com/martintrowland/Scooter/blob/main/Scooter_2_servos.ino
  Lock the leg into this position by screwing the bracket into the servo with the legs in the up position.

## Slide 36: Add testLegs() Routine
/////////////////////////////////////////////////////////////
//-- DIAGNOSTICS ----------------------------------------------//
/////////////////////////////////////////////////////////////
void testLegs() {
Serial.println("Right Leg down");
rightLeg.write(RIGHT_LEG_DOWN, SLOW_SPEED, true);
delay(2000);
Serial.println("Right Leg up");
rightLeg.write(RIGHT_LEG_UP, SLOW_SPEED, true);
delay(2000);
Serial.println("Left Leg Down");
leftLeg.write(LEFT_LEG_DOWN, SLOW_SPEED, true);
delay(2000);
Serial.println("Right Wheel Forward");
rightWheel.write(RIGHT_WHEEL_FORWARD, NA, true);
delay(5000);
rightWheel.write(RIGHT_WHEEL_STOP, NA, true);
Serial.println("Left Wheel Forward");
leftLeg.write(LEFT_WHEEL_FORWARD, NA, true);
delay(5000);
leftLeg.write(LEFT_WHEEL_STOP, NA, true);
}
/////////////////////////////////////////////////////////////
//-- Attach/Detach Servos ----------------------------------------//
/////////////////////////////////////////////////////////////
void attachServos() {
leftWheel.attach(LEFT_WHEEL_PIN);
rightWheel.attach(RIGHT_WHEEL_PIN);
leftLeg.attach(LEFT_LEG_PIN);
rightLeg.attach(RIGHT_LEG_PIN);
}
void detachServos() {
leftWheel.detach();
rightWheel.detach();
leftLeg.detach();
rightLeg.detach();
}

## Slide 37: Add Sonar Routine with Setup and Main
/////////////////////////////////////////////////////////////
//-- Sonar ----------------------------------------------//
/////////////////////////////////////////////////////////////
int sonar(const char *label) {
int Distance = Sonar.ping_cm();
if (Distance == 0) {
Distance = MAX_DISTANCE;
}
if (DEBUG) {
Serial.print(label);
Serial.print(" Ping: ");
Serial.print(Distance);
Serial.println("cm");
}
return Distance;
}
//////////////////////////////////////////////////////////////////
//-- Setup ------------------------------------------------------//
//////////////////////////////////////////////////////////////////
void setup() {
Serial.begin(115200); // Open serial monitor at 115200 baud
}
///////////////////////////////////////////////////////////////////
//-- Principal Loop ---------------------------------------------//
///////////////////////////////////////////////////////////////////
void loop() {
int distance;
DEBUG=true;
Serial.println("Start");
do {
distance = sonar("Main");
}

## Slide 38: Session 3
Robot Design

## Slide 39
Our progress

## Slide 41: Robotic Competitions
B.E.S.T Robotics Design Contest
Botball Educational Robotics Program
FIRST: Robotics Competition
FIRST: Tech Challenge
National Robotics Challenge
Descriptions of these competitions:
https://blog.collegevine.com/5-robotics-competitions-for-high-schoolers/

## Slide 42: The Mering 400 Clears the way for others to follow!
What is it:
A Bristle Bot
2 DC 3V 12000RPM Micro Flat Vibration Motor
Uses vibrating bristles for locomotion
Able to crash into objects easily
What we’ll learn:
Using Pulse Width Modulation to control analog devices
How to trim the toothbrush bristles to promote locomotion
How to create locomotion for a bristle bot
How to tune a bristle bot’s steering
Trim Bristles to form a slant

## Slide 43: Left Foot
Add Left SG90 Servo to the left Leg
Thread cord through slot
Screw servo into left leg bracket.
Add Left FS90R (360) servo to left bracket
Thread the wire through the channel and out the top

## Slide 44: Assemble the Right Leg and Chasis
Repeat the same assembly for the right leg
Insert the legs into the leg chassis
Thread the wires through the slots
The picture shows the back of the chassis
The FS90R wires should thread the front of the chassis
The SG90 wires should be towards the back
Screw the wheels using the 180 degree bracket to the FS90R servos
Do both sides (Left/Right)

## Slide 46: Session 4

## Slide 48: Robotics Careers
The career choices for robotics are almost endless but here are a few examples
  - Automotive Industry
  - NASA
  - Boston Dynamics
  - Software Engineering
  - Consumer Markets
  - Household robots
  - Prosthetics
  - Military

## Slide 49: Education for a Robotics Career
Electrical Engineering (Sensors, computation)
  Control Systems (Mobility)
Computer Engineering (Programming, computation, human-robot interface)
Robotic Engineering (human-robot interface, system integration)
Computer Science (Programming, AI, ML)
Mechanical Engineering (manipulators, mobility)
Bio-Medical Engineering (medical robots)
https://www.youtube.com/watch?v=zauYACP2lOc
OSU Collaborative Robotics Institute

## Slide 50: Session 5

## Slide 51
Our progress

## Slide 53: Put all the tech of the ParksBot, Sauerbot, and crAshleyBot into one and what do you get? The FischBot 500 Able to navigate the challenges
What is it:
An autonomous robot
Utilizes depth sensors and locomotion to avoid obstacles
What we’ll learn:
Algorithms for Obstacle avoidance
How to debug
Challenges in navigation

## Slide 54: FischBot Navigation
Right
Sensor
Left
Sensor
Forward
Right
Sensor
Left
Sensor
WALL
Stop
if an object isn’t close go forward
if an obstacle is really close to both the right and left sensor stop

## Slide 55: FischBot Navigation
Right
Sensor
Left
Sensor
Right
Sensor
Left
Sensor
WALL
Turn Right
Turn Left
WALL
if an object is close to the right sensor turn left
if an object is close to the left sensor turn right

## Slide 56: What’s a Conditional Statment
In English
IF the distance is less than a mile then I’ll walk
ELSE if the distance is less than five miles then I’ll take a bus
ELSE if the distance is less than 100 miles then I’ll drive a car
ELSE take a plane
Examples in Arduino (C Language):
if (condition) {
Action;
}else if (condition) {
Action;
}else {
Action;
}
Condition
Action
If(distance<1){
Serial.println(“let’s walk”);
}else if (distance<5){
Serial.println(“let’s take a bus”);
}else if (distance<100){
Serial.println(“let’s drive”);
else{
Serial.println(“Let’s fly!!”);
}

## Slide 57: Forward
Sonar
Sensor
Forward
const in COLLISION_DISTANCE=40;
distance=sonar();
If (distance>COLLISION_DISTANCE){
wheelsForward(400);
}
If no object is closer than COLLISION_DISTANCE then go Forward
Code
Robot
COLLISION_DISTANCE is the distance in which the object is too close to steer around to avoid.
By experiment this is about 40cm

## Slide 58: STOP
Sonar
Sensor
Stop
COLLISION_DISTANCE
WALL
COLLISION_DISTANCE is the distance in which the object is too close to steer around to avoid.
By experiment this is about 40cm
If an object is closer than the COLLISION_DISTANCE in either the right or left side, then stop
Code
40 cm
|| symbol represent logical OR
const in COLLISION_DISTANCE=40;
distance=sonar();
If (distance>COLLISION_DISTANCE){
wheelsForward(400);
}else{
changeDirection();
}

## Slide 59: STOP
Right
Sensor
Left
Sensor
Stop
COLLISION_DISTANCE
WALL
COLLISION_DISTANCE is the distance in which the object is too close to steer around to avoid.
By experiment this is about 3cm
const in COLLISION_DISTANCE=3;
If ((RightDistance<COLLISION_DISTANCE) ||
(LeftDistance<COLLISION_DISTANCE)){
StandStill(1);
}
If an object is closer than the COLLISION_DISTANCE in either the right or left side, then stop
Code
3cm
|| symbol represent logical OR

## Slide 60: RIGHT TURN
Right
Sensor
Left
Sensor
if an obstacle is really close to both the right and left sensor stop
COLLISION_DISTANCE
TURNING_DISTANCE
TURNING_DISTANCE is the distance in which the robot needs to begin turning to steer around the object
By experiment this is about 15cm
const int TURNING_DISTANCE=15;
If (RightDistance<TURNING_DISTANCE){
GoLeft(3);
}
If an object is within TURNING_DISTANCE on the right side, then turn left
WALL
Code

## Slide 61: LEFT TURN
Right
Sensor
Left
Sensor
if an obstacle is really close to both the right and left sensor stop
COLLISION_DISTANCE
TURNING_DISTANCE
TURNING_DISTANCE is the distance in which the robot needs to begin turning to steer around the object
By experiment this is about 15cm
If an object is within TURNING_DISTANCE on the left side, then turn right
WALL
If (LeftDistance<TURNING_DISTANCE){
GoRight(3);
}
Code

## Slide 62: FORWARD
Right
Sensor
Left
Sensor
if an obstacle is really close to both the right and left sensor stop
COLLISION_DISTANCE
TURNING_DISTANCE
GoForward(2);
If we aren’t turning left, right, or stopping, then there are no objects. Go forward!!
No objects
Code

## Slide 63: Putting It All Together
Right
Sensor
Left
Sensor
Stop
COLLISION_DISTANCE
TURNING_DISTANCE
}else If (RightDistance<TURNING_DISTANCE){
GoLeft(3);
}
If ((RightDistance<COLLISION_DISTANCE) ||
(LeftDistance<COLLISION_DISTANCE)){
StandStill(1);
}
}else{
GoForward(2);
}
}else If (LeftDistance <TURNING_DISTANCE){
GoRight(3);
}

## Slide 64: Tune and Demonstrate your Robot
Can you get your FischBot to navigate through a series of obstacles?
Challenge:
Can you tune your robot to go straight?
Left?
Right?
Challenge:
Can you write code such that your FischBot tries to travel in the same direction while avoiding obstacles?
How would you do it?
Super Challenge:

## Slide 65: BACKUP

## Slide 66: Uninstalling From Macinstosh
A couple of Mac users have said “the driver crashes my mac Sierra how do I uninstall”.
Firstly regards the crash make sure you installed the 1.3 version of the driver, not the old one. You could download it directly from the Manufacturers Website in case they have issued an update since I wrote this page.
Secondly a quick google search reveals that this is how you uninstall:
Open a terminal and type: cd /Library/Extensions/
Verify that the .kext file is present: ls | grep usbserial.kext
Output should be: usbserial.kext
Then type: sudo rm -R usbserial.kext
Verify that the .kext file has been removed: ls | grep usbserial.kext
Output should be empty.
After you should remove the files stored in receipts folder: cd /private/var/db/receipts/
Find the enties: ls | grep usbserial*
Output should be: codebender.cc.ch34xinstaller.usbserial.pkg.bom codebender.cc.ch34xinstaller.usbserial.pkg.plist
Remove each one of the files of the above list: sudo rm -r filename`

## Slide 67: Locomotion Code
#define RIGHT_MOTOR_PIN 5
#define LEFT_MOTOR_PIN 6
#define LEFT_VIBRATE 150
#define RIGHT_VIBRATE 150
#define VIBRATE 150
#define NO_VIBRATE 0
void setup() {
Serial.begin(115200); // Open serial monitor at 115200 baud to see ping results.
pinMode(RIGHT_MOTOR_PIN, OUTPUT);
pinMode(LEFT_MOTOR_PIN, OUTPUT);
delay(5000);
}
void standStill(int seconds) {
analogWrite(RIGHT_MOTOR_PIN, NO_VIBRATE);
analogWrite(LEFT_MOTOR_PIN, NO_VIBRATE);
Serial.println("stop");
delay(seconds * 1000);
}
void turnLeft(int seconds) {
analogWrite(RIGHT_MOTOR_PIN, VIBRATE);
analogWrite(LEFT_MOTOR_PIN, NO_VIBRATE);
Serial.println("turn left");
delay(seconds * 1000);
standStill(0);
}
void turnRight(int seconds) {
analogWrite(RIGHT_MOTOR_PIN, NO_VIBRATE);
analogWrite(LEFT_MOTOR_PIN, VIBRATE);
Serial.println("turn right");
delay(seconds * 1000);
standStill(0);
}
void turnRight(int seconds) {
analogWrite(RIGHT_MOTOR_PIN, NO_VIBRATE);
analogWrite(LEFT_MOTOR_PIN, VIBRATE);
Serial.println("turn right");
delay(seconds * 1000);
standStill(0);
}
void goForward(int seconds) {
analogWrite(RIGHT_MOTOR_PIN, RIGHT_VIBRATE);
analogWrite(LEFT_MOTOR_PIN, LEFT_VIBRATE);
Serial.println("go forward");
delay(seconds * 1000);
standStill(0);
}
void calibrateMovement() {
goForward(5);
standStill(5);
turnLeft(5);
standStill(5);
turnRight(5);
standStill(5);
while (1) {};
}
void loop() {
calibrateMovement();
}

## Slide 68
Classification: Top Secret
Model: Fischbot 605
Name: Scooter Scout

## Slide 69: Navigation Code
Setup
const int TURNING_DISTANCE=15; // in centimeters
const int COLLISION_DISTANCE=3; // in centimeters
Loop
void loop() {
int RightDistance = RightSonar.ping_cm();
if(RightDistance==0){
RightDistance=MAX_DISTANCE;
}
int LeftDistance = LeftSonar.ping_cm();
if(LeftDistance==0){
LeftDistance=MAX_DISTANCE;
}
Serial.print("Left Ping: ");
Serial.print(LeftDistance);
Serial.print(" Right Ping: ");
Serial.print(RightDistance);
Serial.println("cm");
if((RightDistance < COLLISION_DISTANCE) ||
(LeftDistance < COLLISION_DISTANCE)){
standStill(1);
}else if (RightDistance < TURNING_DISTANCE){
turnLeft(3);
}else if (LeftDistance < TURNING_DISTANCE){
turnRight(3);
}else{
digitalWrite(LED_BUILTIN, HIGH);
goForward(2);
digitalWrite(LED_BUILTIN, LOW);
}
}

## Slide 70
FischBot 500
Troop 605
Robotics Merit Badge
Contents:
1 x bread board
1x Arduino Nano CPU
1 x 3 pin switch
1 x 9V Battery with tape
1x 9V Battery Connector
2x HC SR04 Depth Sensors
2x Cell phone motor Vibrators
20x jumper wires
FischBot 500
Troop 605
Robotics Merit Badge
FischBot 500
Troop 605
Robotics Merit Badge
Contents:
1 x bread board
1x Arduino Nano CPU
1 x 3 pin switch
1 x 9V Battery with tape
1x 9V Battery Connector
2x HC SR04 Depth Sensors
2x Cell phone motor Vibrators
20x jumper wires
Contents:
1 x bread board
1x Arduino Nano CPU
1 x 3 pin switch
1 x 9V Battery with tape
1x 9V Battery Connector
2x HC SR04 Depth Sensors
2x Cell phone motor Vibrators
20x jumper wires